## Slide 1
Institute for Human and Machine Cognition
Pensacola, Florida
Simulation Software:
A User’s Experience
Jerry Pratt
December 13, 2016
Simpar
2016 Simulation Grand Challenges Workshop

## Slide 2: Pensacola, FL

## Slide 3: Typical Robot Run

## Slide 4: Typical Robot Run

## Slide 5: Typical Simulation Run

## Slide 6: Typical Simulation
Simulation
Operator Interface
Planner
Visualizer
Perception
Visualizer

## Slide 7: Typical Simulation
Variable Plots
3D Viewport
Overhead Plotter
Variable Entry Boxes

## Slide 8: IHMC Simulation Uses
Roboticists for Virtual Testing.
Roboticists for Virtual Prototyping.
Simulation Researchers Algorithm Implementers.
Roboticists for Machine Learning.
We try to get everything working well in Simulation before running on the real robot.
Usually require some parameter tweaks and tuning on the robot itself.

## Slide 9: Simulation Construction Set
Rigid Body Dynamics: Featherstone Algorithm.
Contact Detection: Point to Surface.
Contact Response: Spring/Dampers with non-linear stiffening z (up) spring.
Stick Slip Friction: Remember touchdown points and slip them when outside of friction cone.
Runge-Kutta 4 or Simple Euler Integrator.
Typically 0.1 msec fixed step time.
Import models:
  Programmatically
  URDF/SDF
20 to 200 Year Old Technology!

## Slide 10: Simulation Construction Set
Runs on Windows, Mac, Linux
Apache 2.0 License
Java
3D World Graphics with Texture Mapping
Record everything. (10,000 variables + typically)
Variable Plots
Easy Visualization
Rewindable
Can programmatically interact with UI.
Easy integration in unit tests.
Plays nicely with other processes.
Usability is Priority #1 for us!

## Slide 11: Simulation Construction Set
Same interaction whether running sim or real robot.
Actuator models: Torque limits, bandwidth, friction.
Sensor models: Camera, Lidar, Joint force/torque, contact sensing.
For complex humanoid approx. 1/2 to 1/6 real time rate depending on whether or not hands and manipulation.
Simulation behaves very similar to real robot in a lot of ways, though things tend to work better in sim due to lack of modeling of stiction, backlash, sensor drift, crappy hardware.

## Slide 12: Features Currently Adding
Better manipulation support.
GJK / EPA Collision Detection.
Combined impulse / spring-damper collision response.
Parallel Processing of collisions.
Manipulation is Becoming More Important for us!

## Slide 13: Grand Challenge: Not Cheat in Simulation
Add time delays.
Add sensor noise.
  High frequency noise.
  Low frequency bias drift.
Add actuator limitations.
  Bandwidth
  Force/torque curve
  Actuator noise, hysteresis, bias drift.
Add stiction, backlash, link compliance.
Walk on unknown, rough ground.

## Slide 14: Grand Challenge: Integration
Simulation
Robot Controller
State Estimator
Sensors.
Sensor Processing.
Perception.
High Level Planning.
User Interface and Interaction.
….
Moore is in retirement. All of these have to run on a separate process to be fast. Comms and Spinup is a challenge.

## Slide 15: Grand Challenge: Easily integrate simulation and real robot
Each time we get a new robot:
    1 week to import model, starting with SolidWorks CAD
    3 months to incorporate low level sensor reading, processing, etc.
Goal:
    1 hour to create and import a model.
    1 week to incorporate sensor reading, processing, etc.

## Slide 16: Grand Challenge: Simulation Validation
Switch between simulation engines seamlessly.
Understand how well simulation is modeling real robot.
Model the robots better, especially noise, stiction, sensor drift, etc.

## Slide 17: Other Thoughts
Run multiple sims in parallel with same controller but different robot parameters to ensure the robustness of a controller to model variation.

## Slide 18
Institute for Human and Machine Cognition
Pensacola, Florida
Simulation Software:
A User’s Experience
Jerry Pratt
December 13, 2016
Simpar
2016 Simulation Grand Challenges Workshop